## Slide 1
Chapter 1
1.1 Introduction
1.2 Computer hardware review
1.3 Operating system concepts

## Slide 2
1.1 Introduction
  What is an operating system
  History of operating systems
  The operating system zoo

## Slide 3
What is an operating system

## Slide 4: Computer system
A computer system consists of
  hardware
  system programs
  application programs

## Slide 5: What is an Operating System
A program that acts as an intermediary between a user of a computer and the computer hardware
System/application programs
Operating system
Hardware
user 1
user 2
user 3
user N
word
processor
spreadsheets
compilers
Web
browsers

## Slide 6: What is an Operating System
System/application programs
Hardware
user 1
user 2
user 3
user N
word
processor
spreadsheets
compilers
Web
browsers
How can I do if there is no Operating system?
Notes: What happens if a computer doesn't have an operating system? Why?

## Slide 7: What is an Operating System
Operating systems are huge, complex, and long-lived
They include at least five million lines of code or more
50 lines/page
1000 pages/book
100 books
Images: clipart-library.com

## Slide 8: What is an Operating System
Window: 70 million lines of code (exclude Internet Explorer, Window Media Player)
50 lines/page
1000 pages/book
10 - 20 bookcases
Images: clipart-library.com

## Slide 9: What is an Operating System
OS is an extended machine
  Hides the messy details which must be performed
  Presents user with a virtual machine, easier to use
OS is a resource manager
  Each program gets time with the resource
  Each program gets space on the resource

## Slide 10
History of Operating Systems

## Slide 11: History of Operating Systems
First generation 1945 - 1955
  vacuum tubes, plug boards
Second generation 1955 - 1965
  transistors, batch systems
Third generation 1965 – 1980
  ICs and multiprogramming
Fourth generation 1980 – present
  personal computers

## Slide 12: History of Operating Systems First generation 1945 - 1955
Computers:ENIAC, UNIVAC…
Operating System: No OS,
Machine Language, plugboards
Single group: designed, built, programmed, operated and maintained each machine

## Slide 13: History of Operating Systems Second Generation 1955 – 1965 (1)
Computers: IBM 1401, IBM 7094…
Operating System : FMS (Fortran Monitor System), IBSYS for Computer 7094
Batch Systems
  Function of Early Batch System
  Structure of a typical FMS job
Separation between designers, builders, programmers, operators and maintenance personnel

## Slide 14: History of Operating Systems Second Generation 1955 – 1965 (2)
Early batch system
  bring cards to 1401
  read cards to tape
  put tape on 7094 which does computing
  put tape on 1401 which prints output

## Slide 15: History of Operating Systems Second Generation 1955 – 1965 (3)
Structure of a typical FMS job – 2nd generation

## Slide 16: History of Operating Systems Third generation 1965 – 1980 (1)
Computers: System/360, IBM370, IBM4300…
Operating System:
  OS/360: to work on all models
  Multiprogamming
  Time Sharing:
    CTSS (Compatible Time Sharing System),
    MULTICS (MULTiplexed Information and Computing Service),
    Unix

## Slide 17: History of Operating Systems Third generation 1965 – 1980 (2)
Multiprogramming system
  three jobs in memory – 3rd generation

## Slide 18: History of Operating Systems Third generation 1965 – 1980 (3)

## Slide 19: History of Operating Systems Fourth generation 1980 – present
Computers: IBM PC 80x86, Macintosh…
Operating System:
  1977: CP/M (Control Program for Microcomputer)
  1980: DOS (Disk Operating System)
  GUI with Macintosh
  1985-1995: Window 3.x
  1995: Window 95
  1996: Window NT 4.0
  1999: Window 2000
  Window 2003
  Unix

## Slide 20
The Operating System Zoo

## Slide 21: The Operating System Zoo
Mainframe operating systems
Server operating systems
Multiprocessor operating systems
Personal computer operating systems
Real-time operating systems
Embedded operating systems
Smart card operating systems

## Slide 22: The Operating System Zoo Mainframe operating systems
  batch
  multiprogrammed
  time-sharing, multitasking
  Application: High-End Web Server, Servers for Business-To-Business transactions
  Example: OS/390

## Slide 23: The Operating System Zoo Server operating systems

## Slide 24: The Operating System Zoo Multiprocessor operating systems
  Multiple CPU
  Share computer bus, clock
  Advantage:
    High system throughput
    High availability
    Multiprocessor system and Multicomputer system

## Slide 25: The Operating System Zoo Personal computer operating systems
  Many I/O devices
  Interface to single user
  Many OS (MS Windows, Mac OS, Solaris, Linux,...).

## Slide 26: The Operating System Zoo Real-time operating systems
  Time is a key parameter
  Two types of real-time system
    Hard real-time system for industrial process control system…
    Soft real-time system for multimedia system

## Slide 27: The Operating System Zoo Embedded operating systems
  Personal digital assistant (PDA): Palm, Pocket-PC, Cellular phones), control devices
  Restriction of memory size, speed of CPU,
  screen size, powers
  Operating System: PalmOS, Windows CE (Consumer Electronic)

## Slide 28: The Operating System Zoo Smart card operating systems
CPU chips on Card
Server processing power and memory constraint
Specific Application:
  Single function: electronic payments
  Multiple function: proprietary systems
  Java oriented: holds interpreter JVM

## Slide 29
1.2 Computer Hardware Review
    - CPU
    - Memory
    - I/O Devices
    - Buses

## Slide 30: Computer Hardware Review
Components of a simple personal computer
Monitor
Bus

## Slide 31: Computer Hardware Review The CPU (1)
PC Program Counter
SP Stack Pointer
PSW Program Status Word
General Registers
Instruction Cycle
Pipeline
Superscalar
System Call

## Slide 32: Computer Hardware Review The CPU (2)

## Slide 33: Computer Hardware Review The CPU (3)
(a) A three-stage pipeline
(b) A superscalar CPU

## Slide 34: Computer Hardware Review The CPU (4)
Dual-mode operation allows OS to protect itself and other system components
  User mode and kernel mode
  Mode bit provided by hardware
    Provides ability to distinguish when system is running user code or kernel code
    Some instructions designated as privileged, only executable in kernel mode
    System call changes mode to kernel, return from call resets it to user

## Slide 35: Computer Hardware Review The CPU (5)
Transition from User to Kernel Mode

## Slide 36: Computer Hardware Review Memory (1)
Typical memory hierarchy
  numbers shown are rough approximations

## Slide 37: Computer Hardware Review Memory (2)
Storage systems organized in hierarchy.
  Speed
  Cost
  Size
  Volatility

## Slide 38: Computer Hardware Review Memory (3)
Registers:
Small number, Fast
Capacity:
  32*32 bit on 32-bit CPU
  64*64 bit on 64-bit CPU

## Slide 39: Computer Hardware Review Memory (4)
Caching – copying information into faster storage system; main memory can be viewed as a last cache for secondary storage.

## Slide 40: Computer Hardware Review Memory (5)
Caching
Important principle, performed at many levels in a computer (in hardware, operating system, software)
Information in use copied from slower to faster storage temporarily
Faster storage (cache) checked first to determine if information is there
  If it is, information used directly from the cache (fast)
  If not, data copied to cache and used there
Cache smaller than storage being cached
  Cache management important design problem
  Cache size and replacement policy

## Slide 41: Computer Hardware Review Memory (6)
Main Memory
RAM (Random Access Memory)
Problem:
  How protect the program from one another and the kernel from them all
  How to handle relocation
Solution: CPU equipped with two special registers
Base Register and Limit Register
MMU (Memory Management Unit) convert Virtual Address to Physical Address
Context Switch; switching from one to another

## Slide 42: Computer Hardware Review Memory (7)
Relocation and Protection
Cannot be sure where program will be loaded in memory
  address locations of variables, code routines cannot be absolute
  must keep a program out of other processes’ partitions
Use base and limit values
  address locations added to base value to map to physical addr
  address locations larger than limit value is an error

## Slide 43: Computer Hardware Review Memory (8)
One base-limit pair and two base-limit pairs

## Slide 44: Computer Hardware Review Memory (9)

## Slide 45: Computer Hardware Review Memory (10)
Other memory in computer
ROM (Read Only Memory)
EEPROM (Electrically Erasable ROM):
  BIOS Basic Input Output System
CMOS:
  Real time clock
  Configuration Information

## Slide 46: Computer Hardware Review Memory (11)
Structure of a disk drive

## Slide 47: Computer Hardware Review Memory (12)
Disk: Cylinder, Track, sector

## Slide 48: Computer Hardware Review I/O Devices (1)
Computer-System Operation
I/O devices and the CPU can execute concurrently.
Each device controller is in charge of a particular device type.
Each device controller has a local buffer.
CPU moves data from/to main memory to/from local buffers
I/O is from the device to local buffer of controller.
Device controller informs CPU that it has finished its operation by causing an interrupt.

## Slide 49: Computer Hardware Review I/O Devices (2)
How interrupts happens. Connections between devices and interrupt controller actually use interrupt lines on the bus rather than dedicated wires

## Slide 50: Computer Hardware Review I/O Devices (3)
Example of Interrupt processing for PC

## Slide 51: Computer Hardware Review I/O Devices (3)
Common Functions of Interrupts
Interrupt transfers control to the interrupt service routine generally, through the interrupt vector table, which contains the addresses of all the service routines.
Interrupt architecture must save the address of the interrupted instruction.
Incoming interrupts are disabled while another interrupt is being processed to prevent a lost interrupt.
A trap is a software-generated interrupt caused either by an error or a user request.
An operating system is interrupt driven.

## Slide 52: Computer Hardware Review I/O Devices (4)
(a) Steps in starting an I/O device and getting interrupt
(b) How the CPU is interrupted
(a)
(b)

## Slide 53: Computer Hardware Review I/O Devices (6)
Operation of a DMA transfer
DMA (Direct Memory Access)

## Slide 54: Computer Hardware Review I/O Devices (7)
DMA
Used for high-speed I/O devices able to transmit information at close to memory speeds.
Device controller transfers blocks of data from buffer storage directly to main memory without CPU intervention.
Only one interrupt is generated per block, rather than the one interrupt per byte.

## Slide 55: Computer Hardware Review
Structure of a large Pentium system

## Slide 56: Computer Hardware Review BUS
Cache BUS
Local BUS
System BUS
ISA Industry Standard Architecture
PCI Peripheral Component Interconnect
USB Universal Serial BUS
SCSI Small Computer System Interface
IDE Integrated Drive Electronic

## Slide 57: Computer Hardware Review Personal Computer (PC)

## Slide 58
1.3 Operating System Concepts
  OS Components
  System calls
  Operating system structure

## Slide 59
OS Components
  Process Management
  Main Memory Management
  File management
  I/O Management
  Secondary Storage Management
  Protection and Security

## Slide 60: Operating System Concepts OS Components (1)
Process Management
  Process is a Program in execution
  A process needs certain resources, including CPU time, memory, files, and I/O devices, to accomplish its task.
  Tasks of process management of OS:
    Process creation and deletion.
    process suspension and resume
    Provision of mechanisms for:
    - Process synchronization
    - Interprocess communication
    - Prevent or avoid deadlock

## Slide 61: Operating System Concepts OS Components (2)
A process tree
  A created two child processes, B and C
  B created three child processes, D, E, and F

## Slide 62: Operating System Concepts OS Components (3)
Two processes connected by a pipe

## Slide 63: Operating System Concepts OS Components (4)
(a) A potential deadlock. (b) an actual deadlock.

## Slide 64: Operating System Concepts OS Components (5)
The Deadlock Problem
A set of blocked processes each holding a resource and waiting to acquire a resource held by another process in the set.
Example
  System has 2 disk drives.
  P1 and P2 each hold one disk drive and each needs another one.

## Slide 65: Operating System Concepts OS Components (6)
Main Memory Management:
  Motivations:
    Increase system performance
    Maximize memory utilization
  Task of main memory of management:
    Keep track of which parts of memory are currently being used and by whom.
    Decide which processes to load when memory space becomes available.
    Allocate and deallocate memory space as needed

## Slide 66: Operating System Concepts OS Components (7)
File management
  File system
    File
    Directory
  Task of file management of OS:
    Create and delete File/Dicrectory
    Manipulate: rename, copy, move, new,…
    Mapping files onto secondary storage.
    File backup on stable (nonvolatile) storage media

## Slide 67: Operating System Concepts OS Components (8)
File system for a university department

## Slide 68: Operating System Concepts OS Components (9)
I/O Management
  Hide the specialty of H/W devices
  Task of I/O Management of OS:
    Manage main memory for the devices using caching, buffering, and spooling
    Maintain and provide a general device-driver interfaces
    Drivers for specific hardware devices.

## Slide 69: Operating System Concepts OS Components (10)
Secondary Storage Management:
  Since main memory (primary storage) is volatile and too small to accommodate all data and programs permanently, the computer system must provide secondary storage to back up main memory.
  Common secondary storage devices: Magnetic disk and Optical disk
  Task of Secondary Storage Management of OS:
    Free space management
    Storage allocation
    Disk scheduling

## Slide 70: Operating System Concepts OS Components (11)
Protection and Security
Protection – any mechanism for controlling access of processes or users to resources defined by the OS
Security – defense of the system against internal and external attacks
  Huge range, including denial-of-service, worms, viruses, identity theft, theft of service

## Slide 71: Operating System Concepts OS Components (12)
Protection and Security
Systems generally first distinguish among users, to determine who can do what
  User identities (user IDs, security IDs) include name and associated number, one per user
  User ID then associated with all files, processes of that user to determine access control
  Group identifier (group ID) allows set of users to be defined and controls managed, then also associated with each process, file
  Privilege escalation allows user to change to effective ID with more rights

## Slide 72: Operating System Concepts Operating System Services
One set of operating-system services provides functions that are helpful to the user:
  User interface - Almost all operating systems have a user interface (UI)
    Varies between Command-Line (CLI), Graphics User Interface (GUI)
  Program execution - The system must be able to load a program into memory and to run that program, end execution, either normally or abnormally (indicating error)
  Control access to I/O device.
  File-system manipulation

## Slide 73: Operating System Concepts Operating System Services
  Communications – Processes may exchange information, on the same computer or between computers over a network
  Error detection – OS needs to be constantly aware of possible errors
  ….

## Slide 74
System Calls
  Making System Calls
  Major POSIX System Calls
  Examples of System Calls

## Slide 75: System Calls Making System Calls (1)
There are 11 steps in making the system call
read (fd, buffer, nbytes)

## Slide 76: System Calls Making System Calls (2)
C program invoking printf() library call, which calls write() system call

## Slide 77: System Calls POSIX System Calls (1)
Some System Calls For Process Management
POSIX (Portable Operating System Interface)

## Slide 78: System Calls POSIX System Calls (2)
Some System Calls For File Management

## Slide 79: System Calls POSIX System Calls (3)
Some System Calls For Directory Management

## Slide 80: System Calls POSIX System Calls (4)
Some System Calls For Miscellaneous Tasks

## Slide 81: System Calls Examples (1)
A stripped down shell:
while (TRUE) { /* repeat forever */
type_prompt( ); /* display prompt */
read_command (command, parameters) /* input from terminal */
if (fork() != 0) { /* fork off child process */
/* Parent code */
waitpid( -1, &status, 0); /* wait for child to exit */
} else {
/* Child code */
execve (command, parameters, 0); /* execute command */
}
}

## Slide 82: System Calls Examples (2)
Processes have three segments: text, data, stack

## Slide 83: System Calls Examples (3)
(a) Two directories before linking /usr/jim/memo to ast's directory
(b) The same directories after linking

## Slide 84: System Calls Examples (4)
(a) File system before the mount
(b) File system after the mount

## Slide 85: System Calls
Some Win32 API calls

## Slide 86
Operating System Structure
  Monolithic system
  Layered System
  Virtual Machine
  Client-server model
  Microkernel

## Slide 87: Operating System Structure Monolithic system (1)
Simple structuring model for a monolithic system

## Slide 88: Operating System Structure Monolithic system (2)
Structure of Operating System:
A main program that invokes the requested service procedure.
A set of service procedures that carry out the system calls.
A set of utility procedures that help the service procedures.

## Slide 89: Operating System Structure Monolithic system (3) : Example
Monolithic
  MS-DOS – written to provide the most functionality in the least space:
    not divided into modules;
    Although MS-DOS has some structure, its interfaces and levels of functionality are not well separated

## Slide 90: Operating System Structure Layered System (1)
Many Layers
Each layer has well defined functions
Upper layer can only calls functions of closely lower layer
Advantages:
  Easier to extend
  Easier to debug from lower to upper layer

## Slide 91: Operating System Structure Layered System (2): Example

## Slide 92: Operating System Structure Layered System (3): Example
Structure of the THE operating system

## Slide 93: Operating System Structure Virtual Machine (1)
Non-virtual machine system model
Virtual machine system model
processes
kernel
hardware
processes | processes | processes
kernel | kernel | kernel
VM1 | VM2 | VM3
Virtual-machine implementation |  | 
hardware |  | 
programming
interface

## Slide 94: Operating System Structure Virtual Machine (2)
A virtual machine takes the layered approach to its logical conclusion. It treats hardware and the operating system kernel as though they were all hardware
A virtual machine provides an interface identical to the underlying bare hardware
The operating system creates the illusion of multiple processes, each executing on its own processor with its own (virtual) memory

## Slide 95: Operating System Structure Virtual Machine (3)
The resources of the physical computer are shared to create the virtual machines
  CPU scheduling can create the appearance that users have their own processor
  Spooling and a file system can provide virtual card readers and virtual line printers
  A normal user time-sharing terminal serves as the virtual machine operator’s console

## Slide 96: Operating System Structure Client-server model (1)
The client-server model

## Slide 97: Operating System Structure Client-server model (2)
The client-server model in a distributed system

## Slide 98: Operating System Structure Microkernel: Example
Microkernel
OS design: The operating system is divided into microkernel (CMU Mach OS - 1980)
  Moves as much from the kernel into “user” space
  kernel  microkernel
  Communication takes place between user modules using message passing.
Application
File
server
X-application
X-window
server
POSIX
application
POSIX
server

## Slide 99: Metric Units
The metric prefixes